============================
d2pro v2.0 (final) - 9 wires
============================

This software is provided as-is, with no warranties of any kind. 
If you use this software, you do so at your own risk!

Thank you for using d2pro!


================
Features / Fixes
================

- Works with DMS, D2A, D2B, D2C and D2C-2 chipset drives

- Adds D2C-2 compatibility to previous d2pro chips that have an SPI Flash

- Enables DVD update of the SPI Flash

- Updatable and configurable via utility disc

- Recovery Mode - can fully recover from a bad flash

- Region Fallback - impossible to brick the drive by setting the wrong region

- Fixes eject issues discovered in previous firmware versions

* This firmware does NOT support the newly-discovered d2e chipsets *


============
Instructions
============

1. If the d2pro chip is already installed in a Wii console then
   disconnect the power cable.

2. Disconnect d2prog from the USB cable.

3. Connect the flat flexible cable to d2prog (and to d2pro if you have
   not done so already).


   Be VERY CAREFUL when connecting the cable and make sure that is in

   place properly. If the cable is misaligned and the Vcc (power) and 

   ground lines are shorted d2pro or d2prog could be damaged.


4. Connect the USB cable to d2prog.

5. Run the updater software. It can be run without parameters for

   fully interactive mode, or with the following switches:


   usage: ./d2prog [-v] [-n] [-y] [-f <num>]

     -v        verify only

     -n        flash only, don't verify

     -y        start flashing immediately

     -f <num>  select firmware


   Run without parameters for fully interactive mode.


   -h brings up the help.   


6. Disconnect USB cable and then d2prog. (done!)